PiWars Z-Gun controller

# Description.
The Z-gun controller board is based on a ATTiny2313 micro controller & 754410 Dual H-Bridge driver IC. It currently supports 2 DC motors (1A) with optional “Single Shot” mode & 2 servo motors with additional GPIO pins for additional functionality if required. Communication with Host controller (Raspberry Pi) is Via I2C interface. The I2C address is stored in EEPROM & can be changed using the In-Circuit Serial Programming (ICSP) header & a standard AVR ICSP suck as an ASPUsb, Arduino or even the Raspberry Pi’s GPIO pins.

# Hardware
The Z-gun interface consist of :-
1)	ATTiny2313 Micro controller
2)	SN754410 Dual H bridge
3)	Various GPIO pins for servo control & “Single Shot Trigger”
## Connections
Conn	Function	AVR Port/Pin	AVR Alternate Functions
J1	I2C connection
J2	ICSP
J3	Motor Power (+5V for DC Motor & Servo’s)
J4	Single Shot Trigger 1	A0	Xtal1
J5	Single Shot Trigger 2	A2	Xtal2
J6	Servo 1
J7	Servo 2
J8	Motor 1
J9	Laser Diode +3.3V output
J10	Motor 2
J11	Unassigned GPIO (D2)
J12	Unassigned GPIO (D0)
J13	Unassigned GPIO (D1)
J14	Unassigned GPIO (D6)