PiWars Z-Gun controller

# Description.
The Z-gun controller board is based on a ATTiny2313 micro controller & 754410 Dual H-Bridge driver IC. It currently supports 2 DC motors (1A) with optional “Single Shot” mode & 2 servo motors with additional GPIO pins for additional functionality if required. Communication with Host controller (Raspberry Pi) is Via I2C interface. The I2C address is stored in EEPROM & can be changed using the In-Circuit Serial Programming (ICSP) header & a standard AVR ICSP suck as an ASPUsb, Arduino or even the Raspberry Pi’s GPIO pins.

# Hardware
The Z-Gun interface consist of :-
1)	ATTiny2313 Micro controller
2)	SN754410 Dual H bridge Driver
3)	Various GPIO pins for servo control & “Single Shot Trigger”
## Connections
Conn	Function	AVR Port/Pin	AVR Alternate Functions
J1	I2C connection
J2	ICSP
J3	Motor Power (+5V for DC Motor & Servo’s)
J4	Single Shot Trigger 1*	A0	Xtal1
J5	Single Shot Trigger 2*	A2	Xtal2
J6	Servo 1
J7	Servo 2
J8	Motor 1
J9	Laser Diode +3.3V output
J10	Motor 2
J11	Unassigned GPIO (D2)
J12	Unassigned GPIO (D0)
J13	Unassigned GPIO (D1)
J14	Unassigned GPIO (D6)

Unassigned GPIO pins are for future expansion.
* A High to Low transition on a “Single Shot” pin will switch off the corresponding motor by setting the mode to 0, the speed setting remains unchanged
## Software
The controller has an I2C interface that has 8 registers on I2cAddress 0x60*
 defined as follows.

Register	Function	Range
0	Motor 1 Speed	0 - 255
1	Motor 2 Speed	0 - 255
2	Motor 1 Direction	0 Stop, 1 Forward, 2 Reverse
3	Motor 2 Direction	0 Stop, 1 Forward, 2 Reverse
4 & 5	Servo1 PWM	~800-2500**
6 & 7	Servo2 PWM	~800-2500**

* The Address is stored in EEPROM and can be changes using the ICSP header if multiple boards are required.
**16 bit value representing the Pulse width of the servo signal in us, stored High Byte, Low Byte & must be written in High Byte Low Byte order to take effect.
## Example Python Module